## Slide 1: Managing embedded generation
Stephen Conner

## Slide 2: How generation is managed
Power stations
Data links
Automatic generation control (AGC) by computer
Embedded generators do not participate in AGC
Notes: Because Egs don’t participate, they can make system behaviour worse. Extra generation should make it better. So they should be made part of the AGC system.
As EG catches on the number of EG units will skyrocket and this system won’t work any more.

## Slide 3: New system is needed for EG
In future there will be too many EG units for a single control centre to handle.
I proposed using many small control centres perhaps in a hierarchy
Etc.
Notes: I decided to look for a way round this problem. I realised that there was no need to bring everything back to a single control centre: a large number of distributed dispatchers could be used instead. The dispatchers would be connected to each other, but in a way that minimised data flow: Each dispatcher would look to its neighbour as if it was just one generator and one demand. So the way it’s wired up in the picture, the national grid centre sees all that EG at the bottom as if it was just one generator.

## Slide 4: In order to work this requires
A way for EG units to “speak” to a computerised control centre
A way for control centres to speak to each other
A way for the control centre to know local demand
A dispatching algorithm for the control centre
All preferably using low-cost proven technologies (PC computers, Ethernet, ISDN, DSL, GSM, etc.)
Notes: Obviously it’s easy enough to say this but making it work is a different matter. All those little dispatchers have to do a job that’s comparable (on load following, AVR, economics, etc) to the single national dispatcher we have just now. But they operate at a handicap because they don’t know what the whole network is doing.
You also need technology to enable it. Getting the dispatchers and generators talking is easy enough, because we have Ethernet, ADSL lines, mobile phones, and so on.Then again, it might not be, because how many CHP engines or whatever have an Ethernet socket and an onboard computer?
Letting each dispatcher know what its local demand is, is more difficult. It can’t go round everyone’s house at 10 second intervals and read the meter! That means you need meters that can report to it electronically, or even smart appliances that do the same.

## Slide 5: The REDMan* dispatching algorithm
Available power
Cost per unit
Rank generators in order of merit
Rank demands in order of merit
Match generation to demand
Dispatching commands
Demand
Buying price
Demand shedding
Generation
Demand
*Real-time Embedded Dispatching Manager
Notes: I created this algorithm based on how the UK Pool (and other countries) works just now. The generators advertise how much power they can put out and how much they want to sell it for. The demands say how much power they want and how much they’re going to pay. It all gets ranked so the cheapest generators are used first and the highest-paying demands are served first. I wrote it in NI LabVIEW.

## Slide 6: Communications
A prototype communication system was made
Uses NI DataSocket over TCP/IP
Operated successfully over Ethernet
Notes: This is the system I made to let my dispatcher talk to generators and demands. I used NI DataSocket which is just a wrapper for TCP/IP. I ran it over Ethernet and also over a dial-up link once.

## Slide 7: Speaking to generators
“Smart Inverter” power electronic interface was developed. It allows small EG/RE units to be dispatched by computer. A totally new concept.
Notes: I mentioned earlier that the dispatcher needs to speak to generators and tell them how much to generate. That can be a problem because a lot of EG hardware is dumb, you turn it on and it just goes off full throttle. As a proof of concept I built this Smart Inverter. It takes commands from a computer, so the dispatcher can turn it up and down as required. So it lets you dispatch inverter-driven stuff like PV, microturbines, batteries, or whatever. As far as I know, this is a first in the embedded generation field.

## Slide 8: Demand measurement
Measuring devices were built for investigative purposes
Soundcard power analyser
“Smart Socket” strip
Notes: I also made the point that it’s difficult to sense demand. So there is a need for a cheap gadget that measures how many watts an appliance or other kind of load is using. Sometimes, in emergencies, you even need to shed demand. I built a few devices to try out some ideas here. The Smart socket strip can tell if the appliance is on, but it can’t measure the wattage. The soundcard analyser works with a laptop and gives a full readout of real power, reactive power, and all the other electrical business. Obviously it’s not cheap by the time you’ve bought the laptop, but it’s just a prototype.

## Slide 9: Proof of Concept Rig
Test rig containing embedded generation (PV), smart inverter, and REDMan software.
Notes: I put all this kit and software together to do a proof of concept. I used PV modules as my embedded generators.This experiment ran for several months last year. I was trying to show that my REDMan software could do dispatching, and that the hardware would do what it said. Again nothing like this had been done before.

## Slide 10: Example results
PV is being dispatched (constrained down)
Notes: I eventually got it to work. Here you can see it’s powering a 50 watt load for four days. So the dispatcher is looking for 50 watts. It buys what it can from the PV, because it’s cheaper than the grid. (I subsidised it.) Whenever the PV makes more than 50 watts, the extra gets dumped.

## Slide 11: Possible future projects
Improve dispatching algorithm
Investigate hierarchy structure, timestepping
Add REDMan modelling to existing power systems simulation software
System studies: dynamics, stability, reliability, economics of REDMan-dispatched system
Notes: I think the results are encouraging but there’s a hell of a lot of work still to do. The dispatcher needs tweaking, the topology and timestepping need a formal mathematical analysis, and it needs a modelling tool so people can do system studies and see how a big REDMan system will behave. So if any of you PhD students want to take it up, see me!

## Slide 12: THE END